## Slide 1: Data Communications for a Global Environment
Lecture 9

## Slide 2: MAC Address Resolution
Problem:
  Unknown MAC address of the next node (whose IP address known)
Solution:
  Uses Address Resolution Protocol (ARP)
Operation
  Broadcast an ARP message to all nodes on a LAN asking which node has a certain IP address
  Host with that IP address then responds by sending back its MAC address
  Store this MAC address in its address table
  Send the message to the destination node
  Example of a MAC address: 00-0C-00-F5-03-5A
Data Communications for a Global Environment

## Slide 3: Routing
Process of identifying what path to have a packet take through a network from sender to receiver
Routing Tables
  Used to make routing decisions
  Shows which path to send packets on to reach a given destination
  Kept by computers making routing decisions
Routers
  Special purpose devices used to handle routing decisions on the Internet
  Maintain their own routing tables
Data Communications for a Global Environment

## Slide 4: Routing Example
Dest.
B
C
D
E
F
G
Next
B
B
D
D
D
B
Routing Table for A
Possible paths from A to G:
  ABCG
  ABEFCG
  ADEFCG
  ADEBCG
B
Each node has its own routing table
A
Data Communications for a Global Environment

## Slide 5: Types of Routing
Centralized routing
  Decisions made by one central computer
  Used on small, mainframe-based networks
Decentralized routing
  Decisions made by each node independently of one another
  Information need to be exchanged to prepare routing tables
  Used by Internet
Data Communications for a Global Environment

## Slide 6: Types of Decentralized Routing
Static routing:
  Uses fixed routing tables developed by network managers
    Each node has its own routing table
    Changes when computers added or removed
  Used on relatively simple networks with few routing options that rarely change
Dynamic routing or Adaptive routing:
  Uses routing tables at each node that are updated dynamically
  Based on routing condition information exchanged between routing devices
Data Communications for a Global Environment

## Slide 7: How would you decide best path?
Data Communications for a Global Environment

## Slide 8: Dynamic Routing Algorithms
Distance Vector
  Uses the least number of hops to decide how to
  route a packet
  Used by Routing Information Protocol (RIP)
Link State
  Uses a variety of information types to decide how to route a packet (more sophisticated)
    e.g., number of hops, congestion, speed of circuit
  Links state info exchanged periodically by each node to keep every node in the network up to date
  Provides more reliable, up to date paths to destinations
  Used by Open Shortest Path First (OSPF) protocol
B
A
C
D
E
F
G
Ex: From A to G  ABCG
Data Communications for a Global Environment

## Slide 9: Routing Protocols
Used to exchange info among nodes for building and maintaining routing tables
Autonomous System (AS)
  A network operated by an organization (e.g., Indiana U.)
  Protocols classified based on autonomous systems
Types of Routing Protocols
  Interior routing protocols (RIP, OSPF, EIGRP, ICMP)
    Operate within a network (autonomous system)
    Provide detailed info about each node and paths
  Exterior routing protocols (BGP)
    Operate between networks (autonomous systems)

## Slide 10: Routing Information Protocol (RIP)
A dynamic distance vector interior routing protocol
Once popular on Internet; now used on simple networks
Operations:
  Manager builds a routing table by using RIP
  Routing tables broadcast periodically (every minute or so) by all nodes
  When a new node added, RIP counts number of hops between computers and updates routing tables

## Slide 11: Open Shortest Path First (OSPF)
A dynamic link state interior routing protocol
Became more popular on Internet
  More reliable paths
    Incorporates traffic and error rate measures
  Less burdensome to the network
    Only the updates sent (not entire routing tables) and only to other routers (no broadcasting)

## Slide 12: Other Interior Routing Protocols
Enhanced Interior Gateway Routing Protocol (EIGRP)
  A dynamic link state protocol (developed by Cisco)
  Records transmission capacity, delay time, reliability and load for all paths
  Keeps the routing tables for its neighbors and uses this information in its routing decisions as well
Internet Control Message Protocol (ICMP)
  Simplest and most basic
  An error reporting protocol (report routing errors to message senders)
  Limited ability to update routing tables

## Slide 13: Exterior Routing Protocols
Border Gateway Protocol (BGP)
  Used to exchange routing info between autonomous systems
  Based on a dynamic distance vector algorithm
  Far more complex than interior routing protocols
  Provide routing info only on selected routes (e.g., preferred or best route)
    Privacy concern
    Too many routes; can’t maintain tables of every single route

## Slide 14
Internet Routing
using
BGP, OSPF and
RIP